## Slide 1
Prolog
Circuit Simulator

## Slide 2: Introduction
Implemented a circuit simulator in Prolog and verified using following circuits
  3 input Full Adder
  5 input Palindrome
  5 input Majority
Implemented Multi-Input AND, OR, XOR gates and single input NOT gate.

## Slide 3: Input Specification
Description of Input wires:
  value(wire_id, value).
Description of a gate (circuit element):
  ckt_elem(elem_id).
  type(elem_id, gate_type).
  inputs(elem_id, number_of_inputs).
Description of connections:
  connected(wire_id1, wire_id2).
  connected(in(input_num, elem_id), wire_id).
  connected(out(elem_id), wire_id).

## Slide 4: Implementation : Predicates Used
are_connected(T1, T2)
  To check if wire T1 and wire T2 are connected.
wire(T)
  To check if T is a wire
  wire can be an input value, an output port or input port of a circuit element
elem_def(G, N)
  To get number of inputs of circuit element G in N
all(G, X)
  To check if all inputs of circuit element G has value X
count(G)
  To check if number of inputs with value 1 are odd

## Slide 5: Implementation : Predicates Used
signal(T, X)
  If T is an assigned value then X gets its value
  If T is an output of a circuit element i.e. out(G) then it is evaluated accordingly
    AND Gate –
      1 if all(G, 1), 0 otherwise
    OR Gate –
      1 if all(G, 0) , 0 otherwise
    NOT Gate –
      1 if input is 0, 0 otherwise
    XOR Gate –
      1 if count(G) , 0 otherwise
  If T is a wire, and there is another wire connected to it then assign the same value to it

## Slide 6: Full Adder Truth Table
X1 | X2 | C1 | Y | C2
0 | 0 | 0 | 0 | 0
0 | 0 | 1 | 1 | 0
0 | 1 | 0 | 1 | 0
0 | 1 | 1 | 0 | 1
1 | 0 | 0 | 1 | 0
1 | 0 | 1 | 0 | 1
1 | 1 | 0 | 0 | 1
1 | 1 | 1 | 1 | 1

## Slide 7: Full Adder Circuit

## Slide 8: Palindrome Truth Table
A | B | C | D | E | Y
0 | 0 | 0 | 0 | 0 | 1
0 | 0 | 0 | 0 | 1 | 0
0 | 0 | 0 | 1 | 0 | 0
0 | 0 | 0 | 1 | 1 | 0
0 | 0 | 1 | 0 | 0 | 1
0 | 0 | 1 | 0 | 1 | 0
0 | 0 | 1 | 1 | 0 | 0
0 | 0 | 1 | 1 | 1 | 0
0 | 1 | 0 | 0 | 0 | 0
0 | 1 | 0 | 0 | 1 | 0
0 | 1 | 0 | 1 | 0 | 1
0 | 1 | 0 | 1 | 1 | 0
0 | 1 | 1 | 0 | 0 | 0
0 | 1 | 1 | 0 | 1 | 0
0 | 1 | 1 | 1 | 0 | 1
0 | 1 | 1 | 1 | 1 | 0

## Slide 9: Palindrome Truth Table
A | B | C | D | E | Y
1 | 0 | 0 | 0 | 0 | 0
1 | 0 | 0 | 0 | 1 | 1
1 | 0 | 0 | 1 | 0 | 0
1 | 0 | 0 | 1 | 1 | 0
1 | 0 | 1 | 0 | 0 | 0
1 | 0 | 1 | 0 | 1 | 1
1 | 0 | 1 | 1 | 0 | 0
1 | 0 | 1 | 1 | 1 | 0
1 | 1 | 0 | 0 | 0 | 0
1 | 1 | 0 | 0 | 1 | 0
1 | 1 | 0 | 1 | 0 | 0
1 | 1 | 0 | 1 | 1 | 1
1 | 1 | 1 | 0 | 0 | 0
1 | 1 | 1 | 0 | 1 | 0
1 | 1 | 1 | 1 | 0 | 0
1 | 1 | 1 | 1 | 1 | 1

## Slide 10: Palindrome Circuit

## Slide 11: Majority Truth Table
A | B | C | D | E | Y
0 | 0 | 0 | 0 | 0 | 0
0 | 0 | 0 | 0 | 1 | 0
0 | 0 | 0 | 1 | 0 | 0
0 | 0 | 0 | 1 | 1 | 0
0 | 0 | 1 | 0 | 0 | 0
0 | 0 | 1 | 0 | 1 | 0
0 | 0 | 1 | 1 | 0 | 0
0 | 0 | 1 | 1 | 1 | 1
0 | 1 | 0 | 0 | 0 | 0
0 | 1 | 0 | 0 | 1 | 0
0 | 1 | 0 | 1 | 0 | 0
0 | 1 | 0 | 1 | 1 | 1
0 | 1 | 1 | 0 | 0 | 0
0 | 1 | 1 | 0 | 1 | 1
0 | 1 | 1 | 1 | 0 | 1
0 | 1 | 1 | 1 | 1 | 1

## Slide 12: Majority Truth Table
A | B | C | D | E | Y
1 | 0 | 0 | 0 | 0 | 0
1 | 0 | 0 | 0 | 1 | 0
1 | 0 | 0 | 1 | 0 | 0
1 | 0 | 0 | 1 | 1 | 1
1 | 0 | 1 | 0 | 0 | 0
1 | 0 | 1 | 0 | 1 | 1
1 | 0 | 1 | 1 | 0 | 1
1 | 0 | 1 | 1 | 1 | 1
1 | 1 | 0 | 0 | 0 | 0
1 | 1 | 0 | 0 | 1 | 1
1 | 1 | 0 | 1 | 0 | 1
1 | 1 | 0 | 1 | 1 | 1
1 | 1 | 1 | 0 | 0 | 1
1 | 1 | 1 | 0 | 1 | 1
1 | 1 | 1 | 1 | 0 | 1
1 | 1 | 1 | 1 | 1 | 1

## Slide 13: Majority Circuit